## Slide 1
INTRODUCTION TO
MASS SPECTROMETRY

## Slide 2
Review: When determining the molecular formula of an unknown
compound, you need the empirical formula (from experiment), and the
molecular mass of the compound, which is typically determined by mass
spectrometry.
Principle is based on separating mixture of atoms and molecules, by mass.

## Slide 3
Imagine throwing a tennis ball, and a ping-pong ball, along parallel
trajectories, into the path of a strong wind. Which ball would be thrown
further off course?
Wind
Wind

## Slide 4
The force that is used to separate atoms and molecules from
one another, by mass, comes from variable magnetic fields.
For the particles to be deflected by a magnetic field, they need
to carry a charge.
CH4 + e- → CH4+ + 2e-
molecule high energy molecular
electron ion
Vaporized molecules of the sample are bombarded with
high energy electrons. The collisions dislodge an electron
from the molecule, producing a species with a charge of
+ 1. Most ions have this charge because it is unlikely for a
molecule to be struck a second time, to produce a + 2 ion.

## Slide 5
Within the magnetic field, molecular ions are separated by their mass/
charge (m/z) ratios. Since most molecules have a + 1 charge, this is
equivalent to separating the species by mass alone. Lighter ions are
deflected more than heavier ones.

## Slide 6
Ions deflected by magnetic field follow a path until they hit a detector.
A signal (current) is generated that is proportional to the number of
impacts with the detector for a particular m/z ratio.
A spectrum is produced where signal intensity (aka “abundance”) is
plotted against m/z ratio (i.e., mass, in most cases). Molecular mass
is determined from the plotted spectra.

## Slide 7
Other factors affecting spectra:
Fragmentation – larger organic molecular ions, especially, tend to break up.
The resultant “carbo-cations” reach detector, producing signals corresponding
to a variety of masses. Because chemical bonds often break in predicable
ways, producing distinct spectral readings, the information provided by these
fragments can assist with structure determination.
Isotopic abundance also plays key roles in explaining resultant spectra.